## Slide 1: The Tradeoff between Energy Efficiency and User State Estimation Accuracy in Mobile Sensing
Yi Wang, Bhaskar Krishnamachari,
Qing Zhao, and Murali Annavaram
Ming Hsieh Department of Electrical Engineering
University of Southern California
Department of Electrical and Computer Engineering
University of California, Davis
MobiCase ‘09
October 26, 2009

## Slide 2: Motivation
The scenario for human-centric, mobile device
based sensing:
Sensors need to be managed intelligently to maintain device/application lifetime
We study two essential but conflicting metrics:
  Energy consumption
  User state estimation accuracy
Notes: Here is a figure showing the current situation of mobile device based human centric sensing. Current technologies enable several sensors and transceivers to be built in to a mobile device , such as acc…. On the higher layer, people are designing a huge amount of useful applications based on mobile sensing such as health monitoring, …
However the ultimate bottleneck is the limit amount of mobile device battery capacity.
It is critical in such applications that sensors need to be managed intelligently to maintain device lifetime.

## Slide 3
Problem modeling and assumptions
The stationary deterministic sensing policy
Estimation of user state for missing observations
Visualizing the tradeoff: energy vs. accuracy
Conclusion and Ongoing/future work
Outline
Notes: 2. A .. Policy that samples user context information

## Slide 4
Model
  Sensor samples the user state
  sequence according to some
  pre-defined policy
  Provide state estimation
  when observations are missing
Assumptions
  Time is discretized
  User state transition is Markovian, with N states
  In each time slot, the sensor can be either “sampling” or “idle”
  If sensor samples
    User state is detected at that time slot
    A corresponding unit of energy is consumed
Preliminaries
Notes:   Mention the tradeoff and say the goal is to identify the tradeoff and find a policy that achieve good tradeoff

## Slide 5
A stationary deterministic sampling policy
“If the sensor detects user state i at some time t, it will stay idle for Ii time slots, and is re-sampled at time slot t+Ii.”
The steady state probability of detecting state i in an observation
Overall expected sampling interval
Define the overall expected energy consumption as:
The Sensing Policy

## Slide 6
Method 1: Picking the most likely state for each time slot in the estimation interval, given neighboring observations
Expected estimation error for time slot t
Expected per-slot estimation error of the whole process
      E[W]: Expected number of incorrect estimations in one estimation interval
      E[N]: Expected number of time slots in one estimation interval
i
j
tm
tm + Ii
?
t
Estimation interval
State Estimation
Notes: In our mechanism, the most likely user state maximizes the probability of..

## Slide 7
Method 2: Estimate the most likely state sequence for the whole estimation interval, given a leading observation
Always find the highest probability path
Expected sequence error for one estimation interval
Expected sequence error for the whole process
i
j
tm
tm + Ii
?
Estimation interval
State Estimation

## Slide 8
Goal: Visualize the tradeoff between energy consumption and expected state estimation error
  By varying Ii, the length of idle intervals
Test policy on two-state discrete time Markov chains
  Different combinations of I1 and I2 are tested (1 ≤ I1 ≤ 30, 1 ≤ I2 ≤ 30)
Six Markov chain transition probability matrices are investigated:
Analytical result vs. Simulation result
  In simulation, user state data is generated based on Markov model
  Policy is applied through the simulation process
  5000 time slots in each simulation run
0.9 0.1
0.1 0.9
0.5 0.5
0.5 0.5
0.9 0.1
0.5 0.5
0.1 0.9
0.9 0.1
0.9 0.1
0.9 0.1
0.5 0.5
0.9 0.1
Case Study
Notes: Finally compare percentages of incorrect estimations vs groud truth

## Slide 9
Expected per-slot estimation error vs. Expected energy consumption
Analytical
Error range: [0, 1-max{π1, π2}]
Result: Method 1
Simulation
Notes: Error decreases as energy increases
Characteristic s are different for different matrices
Best tradeoff

## Slide 10
Expected sequence estimation error vs. Expected energy consumption
Analytical
Error range: [0, 1]
Result: Method 2
Simulation

## Slide 11
An energy budget is given
The optimal stationary deterministic policy can be obtained by
  Searching through all sensing interval combinations
  The one producing the lowest error is selected
Results for two-state Markov chains
Picking the best policy
  Optimal sensing interval sizes vs.
  Energy budget

## Slide 12
A stationary deterministic sensing policy
State estimation mechanisms
Energy efficiency vs. user state estimation accuracy
The optimal stationary deterministic policy can be obtained by exhaustively search
A more computationally efficient algorithm for optimal policy
Performance of sensing policy on real data trace
Conclusion & Ongoing/Future Work

## Slide 13
  More research details available at
  http://anrg.usc.edu
  Please email to
  wangyi@usc.edu